## Slide 1: Machine Learning for Joint Sensing and Communication in Future Millimeter Wave IEEE 802.11 WLANs
Steve Blandino, Tanguy Ropitault, Raied Caromi, Nada Golmie

## Slide 2: Outline
Communication and sensing in mm-wave band.
Turning Wi-Fi devices into motion sensors.
The NIST Q-D framework
ITU AI/ML challenge 2021: sensing with mm-wave communications and ML.

## Slide 3
Communication and sensing in mm-wave band

## Slide 4: Old paradigm: Communication OR sensing
6 GHz
24 GHz
mm-wave
100 GHz
58 GHz
64 GHz
Communication
Sensing
  Multi-Gb/s wireless communications.
  Cm level sensing resolution.

## Slide 5: New paradigm: Communication AND sensing
6 GHz
24 GHz
mm-wave
100 GHz
58 GHz
64 GHz
Communication
Sensing
  Multi-Gb/s wireless communications.
  Cm level sensing resolution.
  Radar waveforms to enable communications
Communication waveforms to enable sensing

## Slide 6: Communication waveforms to enable sensing
6 GHz
24 GHz
mm-wave
100 GHz
58 GHz
64 GHz
Communication
Sensing
  Multi-Gb/s wireless communications.
  Cm level sensing resolution.
  Radar waveforms to enable communications
Communication waveforms to enable sensing

## Slide 7
Turning Wi-Fi devices into motion sensors

## Slide 8: Turn Wi-Fi devices into motion sensors
Transmit signal
Receive signal in monostatic mode
Receive signal in bistatic mode
Ubiquitous WiFi devices:
  Reuse communication devices and protocols to perform sensing.
Sensing can be performed by tracking changes on a wireless channel through the reception of multiple packets over time.
  Time-variations of the channel can be analyzed using signal processing, ML/AI or both.
Device 1
Device 2
Droplets
https://mentor.ieee.org/802.11/dcn/20/11-20-1640-00-00bf-wlan-sensing-usage-model-sneeze-sensing.pptx

## Slide 9: IEEE 802.11bf: WLAN Sensing
IEEE 802.11bf started in Sep/20
  Sub 6GHz and mm-wave.
In mm-wave: use IEEE 802.11ay as a “toolbox” to be used for sensing
  Re-exploit frame structure to enable sensing
  Preamble provides sequences repetition to enable radar-like processing
It will be extended with dedicated procedures for sensing.
Use cases:
  Presence detection, counting number of people, track people location, gesture detection recognition, person identification, vital sign monitoring, in car sensing, fast detection of sleeping drivers, etc.
https://mentor.ieee.org/802.11/documents?is_dcn=DCN%2C%20Title%2C%20Author%20or%20Affiliation&is_group=00bf

## Slide 10: Use case: sensing human presence
Multiple mm-wave WLAN devices working as multi-static radar.
Multiple people moving in an indoor environment.
Indoor sensing:
  Presence detection, number of people in the room, localization of active people.
Application example: audio with user tracking
  Tracking people in a room and pointing the sound of an audio system at them.
WLAN Devices
Moving target

## Slide 11
The NIST Q-D framework

## Slide 12: The NIST Q-D framework
NIST Quasi-Deterministic (Q-D) framework
  Develop simulation models to evaluate IEEE 802.11ad/ay end-to-end (communication) performance with high-fidelity channel, antenna model and system-level protocols.
  Extend the NIST Q-D framework to evaluate IEEE 802.11bf end-to-end performance (communication and sensing) with high-fidelity channel, antenna model and system-level protocols.
5 software packages (https://github.com/wigig-tools)
  NIST Q-D Channel Realization Software
  NIST 802.11ay PHY
  ns-3 802.11ad/ay with Q-D channel
  Codebook Generator
  NIST Q-D Interpreter
NIST
Q-D Interpreter***
ns-3 802.11ad/ay
with Q-D channel**
Codebook Generator*
NIST Q-D Channel Realization software*
NIST 802.11ay PHY*
Channel
PHY
System-Level
Interpretation
Antenna Model
Measurements
* Matlab ** C++ *** Python

## Slide 13: The NIST Q-D framework
NIST
Q-D Interpreter***
ns-3 802.11ad/ay
with Q-D channel**
Codebook Generator*
NIST Q-D Channel Realization software*
NIST 802.11ay PHY*
Channel
PHY
System-Level
Interpretation
Antenna Model
Measurements

## Slide 14: The NIST Q-D Channel realization software
The NIST Q-D Channel Realization software uses the Q-D methodology to generate Multi-Paths Components (MPCs)
  Specular rays: Deterministic approach – Ray tracing (method of images)
  Diffuse components: Stochastic approach using a material library (reflectivity, number of pre-post cursors, etc.)
Channel model for sensing should include:
  Target(s) to be sensed
    Location, trajectory, etc.
IEEE Living Room Scenario

## Slide 15: Target properties
Spatial consistency:
  Both large-scale and small-scale parameters vary with the position of the WLAN nodes, the targets and the environment.
Temporal consistency:
  Large-scale and small-scale parameters are correlated over time when WLAN nodes or targets move.
Complex targets:
  Objects with multiple scattering points: the overall scattering is the sum of all scattering mechanisms from each individual scattering point.

## Slide 16: Complex targets: example human motion
Human micro-doppler signature reflects human motion.
Human walking is a periodic movement.
Human body is highly coordinated: when moving, body parts movements are highly correlated.
Scattering signal from human motion can be modeled as a cluster of scattering points.

## Slide 17: Channel model analysis: human motion scenario
Living room environment (7m×7m×3m).
Bi-static system: 1 TX (-3.9m, 0m, 2.8m) and 1 RX (3m, 0m, 2.8m).
1 target:
  17 centers of scattering (joints).
  Human walking at ~1m/s.
Channel realization rate: 1ms.
Frequency: 60GHz

## Slide 18: Ray tracing results: double directional impulse response
The model captures both the static environment (D-Rays) and the dynamics of the target moving over time (T-Rays).

## Slide 19: Ray tracing results: double directional impulse response
The model captures both the static environment (D-Rays) and the dynamics of the target moving over time (T-Rays).

## Slide 20: Effect of ideal band limitation
Multipath components (MPCs) are merged in fewer taps.
Resample @ 1.76GHz
Resample @ 7.04GHz

## Slide 21
ITU AI/ML 5G challenge 2.0: Where’s waldo?

## Slide 22: Sensing with mm-wave communications and ML
Two MIMO WLAN Access Points working as a bi-static radar.
Multiple dynamic people in an indoor environment.
WALDO (Wireless Artificial intelligence Location DetectiOn): sensing using mmWave communications and ML.
  Presence detection.
  Target localization.
WLAN Access Point
WLAN Access Point
Moving target

## Slide 23: Communication and sensing using signal processing
Channel
Waveform generation and transmitter
Receiver
Presence detection, counting number of people ..
Channel estimation
Range doppler map
Detector
IEEE 802.11ay waveform
Receiver Signal Processing

## Slide 24: Communication and sensing using signal processing
Waveform generation and transmitter
Receiver
Channel
Presence detection, counting number of people ..
Channel estimation
Range doppler map
Detector
Receiver Signal Processing
Channel model with spatial and temporal consistency
IEEE 802.11ay waveform

## Slide 25: Communication and sensing using signal processing
Waveform generation and transmitter
Receiver
Channel
Presence detection, counting number of people ..
Channel estimation
Range doppler map
Detector
Receiver Signal Processing
Channel model with spatial and temporal consistency
Channel estimation
Range-Doppler map
IEEE 802.11ay waveform

## Slide 26: Communication and sensing using ML
Waveform generation and transmitter
Receiver
Channel
Presence detection, counting number of people ..
AI/ML: WALDO
IEEE 802.11ay waveform
Channel model with spatial and temporal consistency

## Slide 27: Where’s WALDO?
A
B
C
D
E
F
G
H
I

## Slide 28: WALDO: we finally found you!
A
B
C
D
E
F
G
H
I
Sector | #people
A | 0
B | 0
C | 0
D | 0
E | 0
F | 0
G | 1
H | 0
I | 0

## Slide 29: Where’s WALDO?
A
B
C
D
E
F
G
H
I

## Slide 30: WALDO: we finally found you!
A
B
C
D
E
F
G
H
I
Sector | #people
A | 0
B | 0
C | 1
D | 0
E | 0
F | 0
G | 1
H | 0
I | 0

## Slide 31: Challenge dataset
NIST Q-D Channel Realization software
Q-D Input
Q-D Output
MPCs (AOA, AOD, Phase, delay and amplitude)
Channel resample at 1.76GHz
Number of targets
Sector of each target
Challenge evaluation
Sector | #people
A | 1
B | 0
C | 0
Provided
Available but not required to solve the challenge
Not provided (Challenge)
Noise
.json
.mat
.txt
AI/ML
Ground Truth
Channel
Waveform generation:
IEEE 802.11ay MIMO-CEF
Static Environment Geometry
2 Static WLAN Sensing Nodes
4 Tx and 4 Rx antennas
Targets: Mobility for every joint
Random number of Targets (1-8)
Each target as a random position, trajectory and velocity
128 channel realizations per scenario (1ms between each realization), 15k scenarios
Received Signal
Number of targets
Sector of each target
Sector | #people
A | 1
B | 0
C | 1
.txt

## Slide 32: Challenge dataset: channel
Q-D channel output (qdChannel/qdOutput#)
  Tx index (index from 0)
  Rx index (index from 0)
  Antenna tx index (index from 0)
  Antenna rx index (index from 0)
  Double directional impulse response
    Delay (s)
    Gain (dB)
    Phase (rad)
    Angle of arrival/departure, azimuth, elevation (Deg)
Available but not required to solve the challenge

## Slide 33: Challenge dataset: get receive signal
Matlab script can be used to generate ML input (receivedSignalGeneration/scriptGenerateRxSig.m) :
  Generate pilot sequence.
  Load channel (qdOutput.json), resample at 1.76GHz
  Transmit pilots on channel.
  Add noise
  Save received signals in .mat files
Available but not required to solve the challenge

## Slide 34: Received signal
Provided
rxSigCh#.mat file (dataset/snr#/rxSigCh#.mat) :
Received signal is a 3D matrix Ns × Na × Nc
    Ns: number of received samples
    Na: number of antennas (4)
    Nc: number of channels (128)

## Slide 35: Challenge dataset: ground truth
.txt file (mlOuput/groundTruth.txt)
  Each row is a vector of chars. Each entry corresponds to a target position.
  The length of the vector is the number of people.
Counting: 8 people
Localization
Sector | #people
A | 1
B | 1
C | 0
D | 2
E | 1
F | 0
G | 1
H | 1
I | 1
Provided

## Slide 36: Challenge evaluation
Counting error:
  Accuracy in counting the total number of people present in the room.
Localization error:
  Accuracy in counting the number of people present in each sector.
Number of targets
Sector of each target
Challenge evaluation
Sector | #people
A | 1
B | 0
C | 0
.txt
Number of targets
Sector of each target
Sector | #people
A | 1
B | 0
C | 1
.txt
Provided

## Slide 37: Challenge evaluation
Final evaluation:
Number of targets
Sector of each target
Challenge evaluation
Sector | #people
A | 1
B | 0
C | 0
.txt
Number of targets
Sector of each target
Sector | #people
A | 1
B | 0
C | 1
.txt
Provided

## Slide 38: Guest Researcher position at NIST
Prize: guest researcher position at NIST

## Slide 39: Communicate and sense at 60GHz
Shed light on passive sensing and localization performance re-using current 5G infrastructure.
Quantify the impact of novel AI/ML techniques with respect to conventional signal processing.
Provide future directions to IEEE standardization activities.

## Slide 40: References
A collection of open-source tools to simulate IEEE 802.11ad/ay WLAN networks in network simulator ns-3. https://github.com/wigig-tools
Q-D simulation & Modeling framework for sensing https://mentor.ieee.org/802.11/dcn/21/11-21-0746-01-00bf-q-d-simulation-modeling-framework-for-sensing.pptx
A preliminary channel model using raytracing to detect human presence https://mentor.ieee.org/802.11/dcn/21/11-21-0747-01-00bf-a-preliminary-channel-model-using-raytracing-to-detect-human-presence.pptx

## Slide 41
Questions?
steve.blandino@nist.gov